## Slide 1
This session introduces the Parcel Fabric API which is in pre-release at 2.5. We’ll cover the information model, concepts and editing patterns. Additionally, we’ll highlight COGO-specific patterns such as using ground to grid corrections and converting between different direction formats.

## Slide 2: ArcGIS Pro SDK for .NET Introduction to the Parcel Fabric API
Please leave artwork “+” clustered.
Do not use them alone, as bullet points, or as a “plus” concept. Thank you.
2020 ESRI DEVELOPER SUMMIT | Palm Springs, CA
Tim Hodson
Ken Galliher

## Slide 3: Session Overview
How to access and use the Pre-release
Conceptual overview
Parcel Editing API for Pro
Coordinate Geometry (COGO)
  Direction Formats and Units
  Ground to Grid Corrections
  Circular arc geometries
Parcel Fabric API

## Slide 4: How to Access and Use the Pre-Release
Tim Hodson

## Slide 5: Pre-release Namespaces
Use Internal Namespaces for Mapping and Editing assemblies
Try it out now
Recompile and re-deploy when Final SDK is released
Internal Namespaces
Notes: NOTE: For the ArcGIS Pro SDK 2.5 parcel fabric API pre-release, parcel fabric objects and methods can be accessed using the internal namespace of the editing and mapping assemblies. This means that the add-ins that you create with the 2.5 pre-release will need to be re-compiled and re-deployed when the parcel fabric portion of the Pro SDK is released as a final product.

## Slide 6: Conceptual Overview

## Slide 7: Conceptual Overview
Parcel Fabric Information Model
Notes: Support for Parcel Fabrics was released in ArcGIS Pro 2.4. This session will be focused on the new SDK, we will be covering it in the context of the data model. Since the fabric is relatively new I’ll do some quick over

## Slide 8: Conceptual Overview
General User Workflow – Order of Operations
General workflow
Order of Operations

## Slide 9: Conceptual Overview
General User Workflow – Order of Operations
Land records document – subdivision plan
  1. Create a Record object
  2. Create COGO lines
  3. Create parcel seeds
  4. Attribute parcel seeds
  5. BUILD Active Record to Complete Parcels

## Slide 10: Conceptual Overview
1. Create New Record
Create a New Record object in the Fabric

## Slide 11: Conceptual Overview
1. Create New Record
Create a New Record object in the Fabric

## Slide 12: Conceptual Overview
2. Create COGO Lines
Create COGO lines

## Slide 13: Conceptual Overview
3. Create Parcel Seeds
Create Parcel Seeds

## Slide 14: Conceptual Overview
3. Create Parcel Seeds
Create Parcel Seeds

## Slide 15: Conceptual Overview
4. Attribute Parcel Seeds
Attribute Parcel Seeds

## Slide 16: Conceptual Overview
4. Attribute Parcel Seeds
Attribute Parcel Seeds

## Slide 17: Conceptual Overview
4. Attribute Parcel Seeds
Attribute Parcel Seeds

## Slide 18: Conceptual Overview
5. BUILD Active Record to Complete Parcels
BUILD Active Record to Complete Parcels

## Slide 19: Conceptual Overview
RECORD polygon footprint
Record geometry updated - polygon footprint

## Slide 20: Parcel Editing API for Pro

## Slide 21: Parcel Editing in Pro
Continued…
Provides course-grained API
Uses and Extends standard Edit Operations framework
Leverages pre-defined information model

## Slide 22: Parcel Editing in Pro
Multi-user environment
  fabric accessed via services
Single use model
  works directly on a file geodatabase
API is designed based on a services architecture
Notes: In a multi-user environment, a parcel fabric is accessed via services and not client-server. As such the parcel fabric API is designed based on a services-only architecture. The parcel fabric also has a single use model that works directly on a file geodatabase.

## Slide 23: Edit Operations - Workflow
Instantiate a new EditOperation
Specify the edit to be performed
Execute the operation

## Slide 24: Parcel Edit Operations - Workflow
Instantiate a new EditOperation
Specify the parcel edit to be performed
Execute the operation

## Slide 25: Parcel Edit Operations - Workflow
Instantiate a new EditOperation
Specify the parcel edit to be performed
Execute the operation

## Slide 26: Parcel Layer
Access the Parcel Fabric via the Parcel Layer
Extension methods
  Set Active Record
  Get Active Record

## Slide 27: Parcel Layer
One parcel layer per map enforced by the system:
Access parcel layer as follows:

## Slide 28: Parcel Fabric - Records
Parcel features contained by the Record

## Slide 29: Parcel Fabric - Records
Parcel features contained by Record

## Slide 30: Parcel Fabric - Points
Notes: Describe points and Fixed points (also called control points etc…) Used for adjustment…

## Slide 31: Parcel Fabric - Points
Creating a fabric point

## Slide 32: Parcel Fabric – Connection Lines
Notes: Connection lines and their purpose…. Much more generically used than in the ArcMap fabric… street centerlines, tie lines from control to parcel points… etc.
All lines in the fabric including those in Parcel Types are COGO enabled.

## Slide 33: Parcel Fabric - Lines
Notes: Connection lines and their purpose…. Much more generically used than in the ArcMap fabric… street centerlines, tie lines from control to parcel points… etc.
All lines in the fabric including those in Parcel Types are COGO enabled.

## Slide 34: Parcel Fabric - Lines
Schema – COGO Enabled lines
COGO Enabled Lines

## Slide 35: Parcel Types
Ken Galliher
Notes: Ken’s turn

## Slide 36: Parcel Fabric Information Model

## Slide 37: Parcel Fabric Information Model
Parcel Types
Parcel Type
The Parcel Fabric is a DML-only API
  Data creation, schema modification, attribute rules etc. via Python
  Geoprocessing tools can be executed from Pro SDK
Notes: A Parcel type consists of a pair of simple feature classes. A line feature class and a polygon feature class. The parcel fabric can have as many parcel types as needed. Tax, Encumbrances, PLSS, easements and any others.
Keep in mind that the parcel fabric API is a DML-only API. Creating new feature classes (or parcel types), extending a parcel type’s schema or adding rules, domains, subtypes and such must be done with Geoprocessing tools or the Pro client.
To accomplish these tasks in a custom application, the Pro SDK has classes to execute any geoprocessing tool or script tool.

## Slide 38: Parcel Fabric Information Model
Parcel Lineage
Parcel Lineage
Merge

## Slide 39: Parcel Fabric Information Model
Parcel Lineage
Parcel Lineage
Merge

## Slide 40: Demo: Creating Parcel Type Creating a Record & Fabric Point Copy Lines To A Parcel Type Merge Parcels
Ken Galliher

## Slide 41: What’s Next for Parcel Fabric API
Tim Hodson

## Slide 42: Enhancements to Parcel Fabric API for Final Release
Simplify Creating and Setting ParcelRecord object
Get Parcel feature sub-layers from Parcel Layer
  Points, Connections & Records feature layers
  Parcel type feature layers (return list of feature layers)
Query feature layer to check if it belongs to the active map’s fabric
Other enhancements…
A few key enhancements planned for Final

## Slide 43: API for Coordinate Geometry (COGO)
Tim Hodson

## Slide 44: Coordinate Geometry (COGO)
COGO Enabled lines
Converting Direction formats and Units
Ground to Grid corrections
Circular arc constructors

## Slide 45: Coordinate Geometry (COGO)
Schema – COGO Enabled lines
COGO Enabled Lines

## Slide 46: Parcel Fabric - Lines
Schema – COGO Enabled lines in the Fabric
COGO Enabled Lines + Parcel Fabric COGO Metadata
COGO Fields ++

## Slide 47: Coordinate Geometry (COGO)
Testing for COGO – Enabled lines
COGO Enabled Lines

## Slide 48: Coordinate Geometry (COGO)
Schema – COGO Enabled lines
COGO Enabled Lines

## Slide 49: Coordinate Geometry (COGO)
Direction Number Format Converts to Quadrant Bearing in display
COGO Enabled Lines
Directions are always stored as
  North Azimuth
  Decimal Degrees

## Slide 50: Coordinate Geometry (COGO)
Direction Units
COGO Enabled Lines
Doubles ?

## Slide 51: Coordinate Geometry (COGO)
Schema – COGO Enabled lines
COGO Enabled Lines

## Slide 52: Coordinate Geometry (COGO)
Converting Direction formats and Units
Traverse Text File example

## Slide 53: Coordinate Geometry (COGO)
Traverse Text File example
Converting Direction formats and Units

## Slide 54: Coordinate Geometry (COGO)
Traverse Text File example
Converting Direction formats and Units

## Slide 55: Coordinate Geometry (COGO)
Using the DirectionUnitFormatConversion class
String Quadrant Bearing to Polar Cartesian

## Slide 56: Coordinate Geometry (COGO)
Using the DirectionUnitFormatConversion class
Polar cartesian radians to North Azimuth decimal degrees

## Slide 57: Coordinate Geometry (COGO)
Traverse Text File example
Converting Direction formats and Units

## Slide 58: Coordinate Geometry (COGO)
Ground to Grid Corrections Tray
Ground to Grid Corrections

## Slide 59: Coordinate Geometry (COGO)
Setting Ground to Grid Corrections properties on the CIM
Ground to Grid Corrections - Setting

## Slide 60: Coordinate Geometry (COGO)
Use extension methods to read Ground to Grid Corrections from the Active Map View
Ground to Grid Corrections - Reading

## Slide 61: Coordinate Geometry (COGO)
Circular arc parameters
Circular Arc Parameters
Shape and Size
  Radius
  Chord Length
  Arc Length
  Delta / Central angle
Orientation
  Chord Direction
  Tangent Direction
  Radial Direction

## Slide 62: Coordinate Geometry (COGO)
Traverse Text File example
Circular Arc Constructors

## Slide 63: Coordinate Geometry (COGO)
Circular arc parameters
Circular Arc Parameters
Shape and Size
  Radius
  Chord Length
  Arc Length
  Delta / Central angle
Orientation
  Chord Direction
  Tangent Direction
  Radial Direction

## Slide 64: Coordinate Geometry (COGO)
Use EllipticArcBuilder to create a Circular Arc
Circular Arc Constructors

## Slide 65: Coordinate Geometry (COGO)
All parameter combinations can be achieved
Circular Arc Constructors

## Slide 66: Coordinate Geometry (COGO)
All parameter combinations can be achieved
Circular Arc Constructors

## Slide 67: Demo – Create A Circular Arc - using ground to grid correction - converting direction and linear units
Tim Hodson

## Slide 68: Demo – Construct Features From COGO Traverse file
Presenter(s)

## Slide 69: Parcel Fabric Resources
Tim Hodson

## Slide 70: Parcel Fabric SDK .Net Resources
Pro Concepts page
  https://github.com/esri/arcgis-pro-sdk/wiki/ProConcepts-Parcel-Fabric
Pro Snippets
  https://github.com/esri/arcgis-pro-sdk/wiki/ProSnippets-ParcelFabric
ArcGISPro-ParcelFabric-PreRelease-APIReference.chm
  https://github.com/esri/arcgis-pro-sdk/releases

## Slide 71: Parcel Fabric SDK .Net Resources
Add-in Sample Code from this presentation

## Slide 72: ArcGIS Pro SDK for .NET Introduction to the Parcel Fabric API
Questions?
    https://github.com/esri/arcgis-pro-sdk/wiki/tech-sessions#2020-palm-springs

## Slide 73: Deployment Patterns
Enterprise Multi-user
  ArcGIS Enterprise (10.7.1 and higher)
  Geodatabase: Enterprise
Single user
  Geodatabase: File