## Slide 1: ArcGIS Pro SDK for .NET : COGO API
Tim Hodson & Ken Galliher
ESRI DEVELOPER SUMMIT 2023

## Slide 2: Session Topics
Overview of COGO (Coordinate Geometry)
COGO Enabled Lines
Units: Directions, Angles & Distances
Ground to Grid Corrections
Creating COGO Lines
  Straight lines
  Circular arcs
  Spiral curves
COGO API

## Slide 3: Overview of COGO (Coordinate geometry)

## Slide 4: Overview of COGO

## Slide 5: Overview of COGO

## Slide 6: Overview of COGO

## Slide 7: COGO Enabled Lines

## Slide 8: COGO Enabled Lines
Schema
COGO Enabled Lines
Notes: All line feature classes that are controlled by the fabric are COGO enabled.
COGO enabled means that these five fields exist on the lines. These fields are there to store Direction and Distance values for straight lines, and also Radius and Arclength values for circular arcs. Spirals are also supported, and so we have a Radius2 field as well.
Whenever a new line feature class is created as part of the fabric we know that it is COGO enabled and it has these fields.

## Slide 9: COGO Enabled Lines
Schema
COGO Enabled Lines
Notes: All line feature classes that are controlled by the fabric are COGO enabled.
COGO enabled means that these five fields exist on the lines. These fields are there to store Direction and Distance values for straight lines, and also Radius and Arclength values for circular arcs. Spirals are also supported, and so we have a Radius2 field as well.
Whenever a new line feature class is created as part of the fabric we know that it is COGO enabled and it has these fields.

## Slide 10: COGO Enabled Lines
Is my line feature class COGO enabled?
COGO Enabled Lines
Notes: COGO-Enabled you can get this property from the FeatureClassDefinition object.

## Slide 11: DEMO: COGO Enabled lines

## Slide 12: Units for COGO values

## Slide 13: Units for COGO values
Linear units
Units for COGO values
Notes: All the attributes that represent lengths such as Distance and Radius, store their values in the Linear Unit of the dataset’s projection.
This is important to note because the map’s projection may be different from the underlying dataset. So that means that the linear unit at the map level may also be different.

## Slide 14: Units for COGO values
Linear units
Units for COGO values
Dataset projection
Notes: All the attributes that represent lengths such as Distance and Radius, store their values in the Linear Unit of the dataset’s projection.
This is important to note because the map’s projection may be different from the underlying dataset. So that means that the linear unit at the map level may also be different.

## Slide 15: Units for COGO values
Linear units
Units for COGO values
Dataset projection
Notes: All the attributes that represent lengths such as Distance and Radius, store their values in the Linear Unit of the dataset’s projection.
This is important to note because the map’s projection may be different from the underlying dataset. So that means that the linear unit at the map level may also be different.

## Slide 16: Units for COGO values
Units for COGO values
Linear units
Getting the linear unit conversion factor
Notes: Here’s some code that uses the same Feature Class definition and gets the Linear Conversion factor. Just a quick note, that if the dataset is in a Geographic coordinate system, then the values are metric.
In this code you can see that is handled by first testing to see if the feature class dataset is projected and then reverting to the default conversion factor of 1 here, if it’s not.

## Slide 17: Units for COGO values
Direction units
North azimuth, decimal degrees
Notes: For Direction values, they are all stored in north azimuth, and in decimal degrees.

## Slide 18: Units for COGO values
Direction units
Units for COGO values
Notes: You will notice that the labeling that you see on the map, and in the other areas of the UI shows values as quadrant bearings, and appears as the formatted text value using arcade in a label expression.
These formats and units are configured and are configurable through the Pro Client. That is topic unto itself, but for the purposes of the API, we know we need to store these directions in the tables as North azimuth decimal degrees.

## Slide 19: Units for COGO values
Converting Direction units & formats
Traverse text file example
Notes: And that brings us to Converting Direction formats and units. We'll use a as an example here a traverse text file and show how to parse through these files in order to generate COGO lines and there's also sample code that we will be providing for you to download and all other samples and demos are available the code is available to you as well.

## Slide 20: Units for COGO values
Converting Direction units & formats
Traverse text file example
Notes: In this traverse file we see that we have a DT code for direction type of quadrant bearing, code QB. … and the DU code is for direction unit, and it is in degrees minutes seconds, DMS.

## Slide 21: Units for COGO values
Converting Direction units & formats
Traverse text file example
Notes: …and here we have an example in this file, of a quadrant bearing that we want to be able to convert into north azimuth, decimal degrees, to store it in the database. So let’s show how to do that through code...

## Slide 22: Units for COGO values
String Quadrant Bearing to Polar Cartesian
Using the DirectionUnitFormatConversion class
Notes: here's a function that converts a quadrant bearing string like the one we saw in the file, to a double value in radians, and in polar cartesian direction format. This is a function that will be used frequently because the geometry engine uses polar radians for its directions.
Looking at this function… it uses a direction unit format conversion class, you create an instance of that, and then you also define a conversion definition object with specific conversion properties. The incoming direction type and direction units are in this case quadrant bearing and degrees minutes seconds, and then the outgoing direction type and directions units are specified here as polar directions in units of radians.
You then call convert to double on the direction unit format converter, passing in the string, and you get back the double in polar radians.

## Slide 23: Units for COGO values
Polar cartesian radians to North Azimuth decimal degrees
Using the DirectionUnitFormatConversion class
Notes: Here's another example … in this case we’re taking in a polar radians value as a double, and spitting out a north azimuth decimal degrees value, also as a double. This is another frequently used function - we’re taking the geometry engine format and storing the direction in the database as our cogo base unit for directions… being north azimuth, decimal degrees.

## Slide 24: Units for COGO values
Getting units from the Project
Getting units from the backstage

## Slide 25: Units for COGO values
Getting units from the Project
Using DisplayUnitFormats class to get the default direction type
Getting Direction units from the backstage

## Slide 26: Units for COGO values
Getting units from the Project
Using DisplayUnitFormats class to get the default direction type
Getting Direction units from the backstage

## Slide 27: DEMO: Converting Direction and Distance Units

## Slide 28: Ground to Grid Corrections

## Slide 29: Coordinate Geometry (COGO)
Ground to Grid corrections
Ground to Grid Corrections
https://pro.arcgis.com/en/pro-app/latest/help/editing/introduction-to-ground-to-grid.htm

## Slide 30: Coordinate Geometry (COGO)
Ground to Grid corrections
Ground to Grid Corrections
https://pro.arcgis.com/en/pro-app/latest/help/editing/introduction-to-ground-to-grid.htm

## Slide 31: Coordinate Geometry (COGO)
Ground to Grid Corrections
Ground to Grid Corrections Tray
Notes: ground to grid corrections … this is what the ground to grid Corrections looks like in the UI. You can see that we can toggle the whole ground to grid correction on or off and then we can individually set to turn on direction offset or distance factors and specify specific numbers for direction offset is an angle and then the distance factor as a constant.

## Slide 32: Coordinate Geometry (COGO)
Ground to Grid Corrections - Reading
Use extension methods to read Ground to Grid Corrections from the Active Map View
Notes: The ground to grid is stored on a per-map basis, each map has its own corrections. Looking at this in code you get your ground to grid via the map view’s CIM definition object.
You can get the ground a grid correction directly off the CIM definition.
Then reading the ground to grid is through extension methods on the ground to grid object.
What these methods do internally is automatically check to see if the ground to grid is active and turned on in the UI and also checks to see what corrections are turned on and currently set by at the user.
If any of those are not active or turned off in the UI, then the scale factor returns one… and similarly for the direction offset correction it returns a value of zero. So from a coding point of view, using these extension methods makes it easy, as you don’t need to check all of those different combinations in the properties.
Also note, here, that the direction offset correction is always stored in decimal degrees … in this little snippet of code we're converting it to radians for use in the geometry engine functions.

## Slide 33: Coordinate Geometry (COGO)
Ground to Grid Corrections - Setting
Setting Ground to Grid Correction properties on the CIM
Notes: Similar pattern, for setting the ground to grid, but a few additional things to note. In the case of a brand new map, as indicated in the comments here you would need to initialize it for the first time so if it's null then you can create it.
Also, there are no extension methods needed in this case, you just set the properties directly. Looking at what the code is doing here, it’s turning on a constant scale factor to a value… represented by the dScaleFactor variable. You can see the UI equivalents shown in the comments of what pieces of the UI those are represented by… Then this last line shown here is setting the ground to grid correction with that new ground to grid object.

## Slide 34: Creating COGO Lines

## Slide 35: Creating COGO Lines
COGO Lines
Straight Lines
Circular Arcs
Spiral Curves

## Slide 36: Creating COGO Lines
Straight Line properties
Straight Line Parameters
Shape and Size
  Length
Orientation
  Direction

## Slide 37: Creating COGO Lines
Straight Line properties
Straight Line – part 1

## Slide 38: Creating COGO Lines
Straight Line properties
Straight Line – part 2

## Slide 39: Creating COGO Lines
Circular Arc Parameters
Shape and Size
  Radius
  Chord Length
  Arc Length
  Delta / Central Angle
Orientation
  Chord Direction
  Tangent Direction
  Radial Direction
Circular arc parameters
Notes: For circular arcs these are the typical parameters we use when creating them. For the shape and size of the arc we are looking at combinations of any two of the radius, chord length, arc length, or the delta.
For the orientation of that curve it’s defined by any one of those three parameters being chord direction… tangent direction … or radial direction.

## Slide 40: Creating COGO Lines
Circular Arc Parameters
Traverse text file - circular arc
Notes: Here's an example again going back to that traverse file.

## Slide 41: Creating COGO Lines
Circular arc parameters
Circular Arc Parameters
Shape and Size
  Radius
  Chord Length
  Arc Length
  Delta / Central Angle
Orientation
  Chord Direction
  Tangent Direction
  Radial Direction
Notes: in this case for our two shape and size parameters we have a radius and a central angle, and for the orientation parameter we’re using a tangent direction.

## Slide 42: Creating COGO Lines
EllipticArcBuilder creates Circular arcs
Circular Arc Constructors
Notes: Circular arcs can be created via the API using the CreateCircularArc method on the EllipticArcBuilderEx class. The circular arc is really just a special form of an elliptical arc with minor and major axes the same length and so there are functions on this class specifically for creating circular arcs. In this case you can see that we're using a chord length, a chord bearing, a radius and counterclockwise curve to the left as a minor for the circular arc.

## Slide 43: Creating COGO Lines
All parameter combinations can be achieved
Circular Arc Constructors
Notes: You can achieve all of the different parameter combinations just using some first principle circular arc geometry, as shown here. In this instance we're creating a circular arc using a delta, an arc length and the chord bearing. You can see that we are pre-computing our radius and chord length from the arc length and Delta, the Delta is also called the central angle. With these we can then use the same constructor again for the circular arc, even though the initial parameters are different.

## Slide 44: Creating COGO Lines
Circular Arc Constructors
All parameter combinations can be achieved
Notes: …and here's another example starting with different initial parameters. Here we’re using the radial bearing, central angle and radius, to pre calculate the chord bearing and distance, and so on.
All of these different parameter combinations are available in the sample code that I’ll demonstrate in a few minutes, and that you’ll have access to through the download.

## Slide 45: Creating COGO Lines
Spiral parameters
Spiral Curve Parameters
  Radius 1
  Radius 2
  Arc Length
  Chord Direction

## Slide 46: Creating COGO Lines
Spiral parameters
Spiral Curve Parameters
  Radius 1
  Radius 2
  Arc Length
  Chord Direction

## Slide 47: Creating COGO Lines
Spiral parameters
Spiral Curve Parameters
  Radius 1
  Radius 2
  Arc Length
  Chord Direction

## Slide 48: Creating COGO Lines
Spiral parameters
Spiral Curve Parameters
  Radius 1
  Radius 2
  Arc Length
  Chord Direction

## Slide 49: DEMO: Creating COGO Features
Putting it all together

## Slide 50: Parcel Traverse & COGO Loop Traverse

## Slide 51: Parcel Edges
Segment
Parcel Edge
Segment
Segment
Segment
The parcel polygon geometry is used to define parcel edges
Parcel edges are established based on segment tangency
Each sequence of tangent segments define a parcel edge

## Slide 52: Parcel Edges
The parcel polygon geometry is used to define parcel edges
Parcel edges are established based on segment tangency
Each sequence of tangent segments define a parcel edge
Segment
Parcel Edge
Segment
Segment
Segment
Parcel Edge

## Slide 53: Parcel Edges – Clockwise Sequence
Edge 4
Edge 1
Edge 2
Edge 3
Start

## Slide 54: Parcel Line-to-Edge Relationships
Enumeration & Booleans (qualitative)
Geometry (quantitative)

## Slide 55: Parcel Line-to-Edge Relationships
Enumeration
Start Vertex Match At an Edge End
End Vertex Match At an Edge End
Start Vertex On an Edge
End Vertex On an Edge
Boolean
Is Reversed
Has Next Line Connectivity
Examples of some qualitative relationships

## Slide 56: Parcel Line-to-Edge Relationships
Examples of some qualitative relationships
Edge 2 has 3 lines

## Slide 57: Parcel Line-to-Edge Relationships
Examples of some qualitative relationships
Edge 2 has 3 lines: A, B, and C
Edge 2
A
B
C

## Slide 58: Parcel Line-to-Edge Relationships
Start Vertex Matches An Edge End
End Vertex Matches An Edge End
Start Vertex On an Edge
End Vertex On an Edge
Line Direction Is Clockwise
Example of a qualitative Line-to-Edge relationship

## Slide 59: Parcel Line-to-Edge Relationships
Line Direction Is Clockwise
Example of a qualitative Line-to-Edge relationship
A
B
C

## Slide 60: Parcel Line-to-Edge Relationships
Enumeration & Booleans (qualitative)
Geometry (quantitative)

## Slide 61: Parcel Line-to-Edge Relationships
Geometry
Edge length proportion
Quantitative Line-to-Edge relationships

## Slide 62: Parcel Line-to-Edge Relationships
Geometry
Edge length proportion
Quantitative Line-to-Edge relationships

## Slide 63: Parcel Line-to-Edge Relationships
Geometry
Edge length proportion
A
B
C
Quantitative Line-to-Edge relationships

## Slide 64: Parcel Line-to-Edge Relationships
Geometry
Edge length proportion
B
Quantitative Line-to-Edge relationships

## Slide 65: Parcel Line-to-Edge Relationships
Geometry
Edge length proportion
Quantitative Line-to-Edge relationships
C

## Slide 66: Parcel Line-to-Edge Relationships
Geometry
Edge length proportion
Quantitative Line-to-Edge relationships
B

## Slide 67: Parcel Line-to-Edge Relationships
Enumeration & Booleans (qualitative)
Geometry (quantitative)
LINK

## Slide 68: Parcel Fabric .Net API 3.0
Navigate parcel line and point elements
Extension method GetSequencedParcelEdgeInfoAsync
Returns ParcelEdgeCollection object

## Slide 69: Parcel Fabric .Net API 3.0
Navigate parcel line and point elements
Work with the lineInfo objects returned from each Edge

## Slide 70: Resources – ArcGIS Pro SDK for .NET COGO API
Notes: That brings us to the end of the session, but before we end, here are some resources…

## Slide 71: Resources - ArcGIS Pro SDK for .NET : COGO API
Pro Concepts page
  https://github.com/esri/arcgis-pro-sdk/wiki/ProConcepts-COGO
  https://github.com/esri/arcgis-pro-sdk/wiki/ProConcepts-Parcel-Fabric#get-clockwise-sequenced-parcel-edge-information
Notes: …there is a pro concepts page that you can get to from this link and this goes through a lot of what you've seen here today and that includes the code snippets you saw in this session, and many others as well…

## Slide 72: ArcGIS Pro SDK for .Net COGO
Questions?
    https://github.com/Esri/arcgis-pro-sdk/wiki/Tech-Sessions#2023-palm-springs
Notes: …and then there's also all the sample code and data from this presentation … it is all available to you … here… via this link or QR code
At that location you will find a folder called “COGO API” and from that you can get this content.

## Slide 73
Download the Esri Events app and find your event
Select the session you attended
Scroll down to “Survey”
Log in to access the survey
Please Share Your Feedback in the App

## Slide 74: ArcGIS Pro SDK for .NET – Technical Sessions
NOTE: Session titles are led by “ArcGIS Pro SDK for .NET” in online agenda
Detailed Agenda: https://www.esri.com/en-us/about/events/devsummit/agenda/detailed
Date | Time | Session
Tue, Mar 7 | 2:00 p.m. - 3:00 p.m. | ArcGIS Pro SDK for .NET: Customizing Layout
 | 4:00 p.m. - 5:00 p.m. | ArcGIS Pro SDK for .NET: Intermediate Editing 1
 | 5:30 p.m. - 6:30 p.m. | ArcGIS Pro SDK for .NET: Intermediate Editing 2
Wed, Mar 8 | 10:30 a.m. - 11:30 a.m. | What's New in the Geodatabase and Utility Network APIs
Thu, Mar 9 | 10:30 – 11:30 am | ArcGIS Pro SDK for .NET: Intermediate Data Visualization Using Table Controls
 | 1:00 p.m. - 2:00 p.m. | ArcGIS Pro SDK for .NET: Intermediate Map Visualization Using Time API and Tray Item Template
Fri, Mar 10 | 8:30 a.m – 9:30 a.m | ArcGIS Pro SDK for .NET: Parcel Fabric API
 | 10:00 a.m – 11:00 a.m | ArcGIS Pro SDK for .NET: COGO API and Parcel Traverse

## Slide 75: ArcGIS Pro SDK for .NET – Demo theaters
NOTE: Session titles are led by “ArcGIS Pro SDK for .NET” in online agenda
Detailed Agenda: https://www.esri.com/en-us/about/events/devsummit/agenda/detailed
Date | Time | Session
Wed, Mar 8 | 4:00 p.m. - 4:30 p.m. | ArcGIS Pro SDK for .NET: How to Run GP Tools from Your Add-in
 | 4:45 p.m. - 5:15 p.m. | ArcGIS Pro SDK for .NET: Customize Galleries and Comboboxes with Templates
 | 5:30 p.m. - 6:00 p.m. | ArcGIS Pro SDK for .NET: Customizing the Editor Attributes Pane
The Road Ahead: ArcGIS Pro
Date | Time | Session
Thu, Mar 9 | 2:30 p.m. - 3:30 p.m. | ArcGIS Pro: The Road Ahead

## Slide 76
ESRI DEVELOPER SUMMIT 2023

## Slide 77
Copyright © 2023 Esri. All rights reserved.