## Slide 1: ArcGIS Pro SDK for .NET Introduction to the 3D Analyst API
Uma Harano
Narelle Chedzey
2024 ESRI DEVELOPER SUMMIT
Notes: Esri Corporate Template-Dark v4.3
September 27, 2023

## Slide 2: Session Overview
3D Datasets – TIN, Terrain, LAS
TIN elements / Searching
Layers + layer creation
Renderers
Line of Sight (TIN)
LAS

## Slide 3: TIN
Form of vector-based digital geographic data that represents continuous surfaces such as terrain elevation or temperature gradients
Constructed by triangulating a set of nodes (points). The nodes are connected by a series of edges to form a network of contiguous, nonoverlapping triangles
Stored as a series of standalone files in a folder on disk
Connect using FileSystemConnectionPath, FileSystemDatastoreType.Tin and FileSystemDatastore
string path = @"d:\Data\Tin";
var fileConnection = new FileSystemConnectionPath(new Uri(path),
FileSystemDatastoreType.Tin);
using (FileSystemDatastore dataStore = new FileSystemDatastore(fileConnection))
{
}

## Slide 4: TIN
Use OpenDataset to obtain the TinDataset object
Use GetDefinition to obtain the TinDatasetDefinition object
string path = @"d:\Data\Tin";
var fileConnection = new FileSystemConnectionPath(new Uri(path), FileSystemDatastoreType.Tin);
using (FileSystemDatastore dataStore = new FileSystemDatastore(fileConnection))
{
// TIN is in a folder at d:\Data\Tin\TinDataset
string dsName = "TinDataset";
using (var tin = dataStore.OpenDataset<TinDataset>(dsName)) {
}
using (var tinDef = dataStore.GetDefinition<TinDatasetDefinition>(dsName))
{
}
}

## Slide 5: TIN
Useful methods (TinDataset)
  Triangulation technique – UsesConstrainedDelaunay
  Data area – GetDataArea
  SuperNodeExtent - GetSuperNodeExtent
  Counts – GetNodeCount, GetOutsideNodeCount, GetEdgeCount, GetOutsideEdgeCount, GetTriangleCount, GetOutsideTriangleCount
// get the super node extent
var superNodeExtent = tin.GetSuperNodeExtent();
// get the data area
var dataArea = tin.GetDataArea();
// counts
var nodeCount = tin.GetNodeCount();
var nodeOutside = tin.GetOutsideNodeCount();
var triangleCount = tin.GetTriangleCount();
var triangleOutside = tin.GetOutsideTriangleCount();

## Slide 6: Terrain
A multiresolution TIN based surface. That is, it consists of a series of TINs, each used within a specific map scale range.
  Coarse grained TIN when zoomed out. Finer grained TIN (more level of detail) when zoomed in.
Measurements are typically LiDAR, photogrammetric sources.
Stored in the geodatabase inside a feature dataset.
Connect using FileGeodatabaseConnectionPath and Geodatabase
string path = @"d:\Data\Terrain\filegdb_Containing_A_Terrain.gdb";
var fileConnection = new FileGeodatabaseConnectionPath(new Uri(path);
using (Geodatabase gdb = new Geodatabase(fileConnection))
{
}

## Slide 7: Terrain
Use OpenDataset to obtain the Terrain object
Use GetDefinition to obtain the TerrainDefinition object
string path = @"d:\Data\Terrain\filegdb_Containing_A_Terrain.gdb";
var fileConnection = new FileGeodatabaseConnectionPath(new Uri(path);
using (Geodatabase gdb = new Geodatabase(fileConnection)) {
string dsName = "nameOfTerrain";
using (var terrain = gdb.OpenDataset<Terrain>(dsName)) {
}
using (var terrainDef = gdb.GetDefinition<TerrainDefinition>(dsName))
{
}
}

## Slide 8: Terrain
Useful methods (Terrain)
  Parent feature dataset – GetFeatureDataset
  Participating feature classes – GetDataSources
    TerrainDataSource class – name of the data source and information about how the features are used to define the terrain surface through a range of scales
  Pyramid level information – GetPyramidLevels
    TerrainPyramidLevel class – resolution and display scale at which the level becomes active
Useful methods (TerrainDefinition)
  Pyramid type – GetPyramidType
  Pyramid properties - GetPyramidWindowSizeProperties

## Slide 9: Terrain
// get the participating feature classes
IReadOnlyList<TerrainDataSource> dataSources = terrain.GetDataSources();
foreach (var ds in dataSources)
{
var dsName = ds.DataSourceName;
var surfaceType = ds.SufaceType;
var maxResolution = ds.MaximumResolution;
var minResolution = ds.MinimumResolution
}
// get the pyramid levels
IReadOnlyList<TerrainPyramidLevel> pyramidLevels = terrain.GetPyramidLevels();
foreach (var pyramidLevel in pyramidLevels)
{
var resolution = pyramidLevel.Resolution;
var maxScale = pyramidLevel.MaximumScale;
}
// get the pyramid type
var pyramidType = terrainDefinition.GetPyramidType();

## Slide 10: LAS
Format for storing airborne LiDAR data.
Collection of LAS files is a LAS dataset (.lasd)
Stored as a series of standalone files on disk
Connect using FileSystemConnectionPath, FileSystemDatastoreType.LasDataset and FileSystemDatastore
string path = @"d:\Data\LASDataset";
var fileConnection = new FileSystemConnectionPath(new Uri(path),
FileSystemDatastoreType.LasDataset);
using (FileSystemDatastore dataStore = new FileSystemDatastore(fileConnection))
{
}

## Slide 11: LAS
Use OpenDataset to obtain the LasDataset object
Use GetDefinition to obtain the LasDatasetDefinition object
string path = @"d:\Data\LASDataset ";
var fileConnection = new FileSystemConnectionPath(new Uri(path),
FileSystemDatastoreType.LasDataset);
using (FileSystemDatastore dataStore = new FileSystemDatastore(fileConnection)) {
string dsName = "somedataset.lasd";
using (var las = gdb.OpenDataset<LasDataset>(dsName)) {
}
using (var lasDef = gdb.GetDefinition<LasDatasetDefinition>(dsName))
{
}
}

## Slide 12: LAS
Useful methods (LasDataset)
  Individual LAS files – GetFiles, GetFileCounts
    LasFile class
  Surface constraints - define how the constraint features are incorporated into the triangulation of the surface; e.g. breaklines - GetSurfaceConstraints
    SurfaceConstraint class
  Classification codes – GetUniqueClassCodes
  Returns – GetUniqueReturns

## Slide 13: LAS
// get individual file information
var (lasFileCount, zLasFileCount) = lasDataset.GetFileCounts();
var fileInfo = lasDataset.GetFiles();
foreach (var file in fileInfo) {
var path = file.FilePath;
var name = file.FileName;
var ptCount = file.PointCount;
var zMin = file.ZMin;
var zMax = file.ZMax;
}
// get the surface constraints
IReadOnlyList<SurfaceConstraint> constraints = lasDataset.GetSurfaceConstraints();
foreach (var constraint in constraints) {
var dsName = constraint.DataSourceName;
var wksPath = constraint.WorkspacePath;
var heightfield = constraint.HeightField;
var surfaceType = constraint.SurfaceType;
}
// get unique classification codes, return values
var classCodes = lasDataset.GetUniqueClassCodes();
var returns = lasDataset.GetUniqueReturns();

## Slide 14: Datasets
Namespace – ArcGIS.Core.Data.Analyst3D
 | TIN | Terrain | LAS
Data Format | Standalone files in a folder | Geodatabase | Standalone files
Connection Objects | FileSystemConnectionPath FileSystemDatastore | FileGeodatabaseConnectionPath Geodatabase | FileSystemConnectionPath FileSystemDatastore
Dataset objects | TinDataset | Terrain | LasDataset
Definition objects | TinDatasetDefinition | TerrainDefinition | LasDatasetDefinition

## Slide 15: TIN
Super nodes
  4 generated points that are used in the initial construction of the TIN. They reside outside the declared data extent.
Super node extent
  Maximum bounding rectangle that surrounds the 4 super nodes
Super nodes = green circles
Super node extent = red boundary

## Slide 16: TIN
Inside vs Outside
  Elements are classified as inside or outside the TIN’s data area.
  Initially only the 4 super nodes and their incident edges and triangles are outside. All other elements are inside.
  If clip or erase polygons are added to a TIN, they modify what elements are considered inside or outside.
Data area / interpolation zone
  The boundary between inside and outside elements.
Super nodes = green circles
Super node extent = red boundary
Data area = black boundary
Inside elements (edges) = dark green lines
Outside elements (edges) = purple lines

## Slide 17: TIN Elements
3 different element types
  Nodes – TinNode
  Edges – TinEdge
  Triangles - TinTriangle
Abstract Base Class – TinElement
  ElementType
  Index (base index is 1. Not 0)
  IsInsideDataArea (inside vs outside)

## Slide 18: TIN Elements
TinNode
  Stores x, y, z values
    Coordinate2D, Coordinate3D, ToMapPoint
  Connectivity information
    GetAdjacentNodes, GetIncidentEdges, GetIncidentTriangles

## Slide 19: TIN Elements
TinEdge
  Comprised of 2 Nodes
    Nodes property
  Geometry – ToPolyline
  EdgeType – regular, hard, soft
  Connectivity information
    GetNeighbor, GetNextCounterClockwiseEdge, GetNextClockwiseEdge, GetNextEdgeInTriangle, GetPreviousEdgeInTriangle, LeftTriangle, RightTriangle

## Slide 20: TIN Elements
TinTriangle
  Comprised of 3 nodes and 3 edges oriented in a clockwise direction
    Nodes, Edges properties
  Geometry – ToPolygon
  Other properties
    Aspect, Intensity, Slope
    GetCentroid, GetCircumCircle, GetNormal
  Connectivity information
    GetAdjacentTriangles

## Slide 21: Accessing TIN Elements
Using Element Index
  GetNodeByIndex, GetEdgeByIndex, GetTriangleByIndex
// get the specific node, edge, triangle
using (TinNode node = tinDataset.GetNodeByIndex(23)) {
...
}
using (TinEdge edge = tinDataset.GetEdgeByIndex(45)) {
...
}
using (TinTriangle triangle = tinDataset.GetTriangleByIndex(22))
...
}

## Slide 22: Accessing TIN Elements
Using a MapPoint
  GetNearestNode, GetNearestEdge, GetTriangleByPoint
// get the nearest node, edge, triangle
using (TinNode nearestNode = tinDataset.GetNearestNode(identifyPoint)) {
...
}
using (TinEdge nearestEdge = tinDataset.GetNearestEdge(identifyPoint)) {
...
}
using (TinTriangle nearestTriangle = tinDataset.GetTrianglebyPoint(identifyPoint)) {
...
}

## Slide 23: Accessing TIN Elements
Search with a filter
  SearchNodes, SearchEdges, SearchTriangles
  Similar pattern to searching a feature class for features
    Parameter is a filter object – TinNodeFilter, TinEdgeFilter, TinTriangleFilter
      Pass null to find all elements in the TIN’s data extent
    Returns a cursor – TinNodeCursor, TinEdgeCursor, TinTriangleCursor
// search for nodes
using (TinNodeCursor nodeCursor = tinDataset.SearchNodes(null))
{
while (nodeCursor.MoveNext())
{
using (ArcGIS.Core.Data.Analyst3D.TinNode node = nodeCursor.Current)
{
}
}
}

## Slide 24: TIN Filters
FilterEnvelope
  Specify an extent to search. Default is null meaning the TIN’s data extent is used.
DataElementsOnly
  Specify if you with to return “inside” elements only. False can return “outside” elements and / or super nodes depending upon the FilterEnvelope and FilterType. Default is false.
FilterType
  Specify the type of search to perform. Search All, InsideTin, InsideDataArea. Default is All.
** Combine FilterType and DataElementsOnly to control the types of elements returned.

## Slide 25: TIN Filters
// search for “inside” edges in an extent
TinEdgeFilter edgeFilter = new ArcGIS.Core.Data.Analyst3D.TinEdgeFilter();
edgeFilter.FilterEnvelope = extent;
edgeFilter.DataElementsOnly = true;
// edgeFilter.FilterType = TinFilterType.All; // default
// search edges inside data area within an extent
// Elements inside the TIN’s data area are by definition “inside” so DataElementsOnly
// property is not required.
TinEdgeFilter edgeFilter = new ArcGIS.Core.Data.Analyst3D.TinEdgeFilter();
edgeFilter.FilterEnvelope = extent;
edgeFilter.FilterType = TinFilterType.InsideDataArea;
// search for edges in an extent – this could include “outside” elements depending on extent
TinEdgeFilter edgeFilter = new ArcGIS.Core.Data.Analyst3D.TinEdgeFilter();
edgeFilter.FilterEnvelope = extent;
// edgeFilter.DataElementsOnly = false; // default
// edgeFilter.FilterType = TinFilterType.All; // default

## Slide 26: TIN Filters
TinNodeFilter
  Search for super nodes using SuperNode property
    ** Set DataElementsOnly to false. FilterEnvelope to super node extent
TinEdgeFilter
  Search by edge type using FilterByEdgeType and EdgeType properties
// search for super nodes only
var nodeFilter = new ArcGIS.Core.Data.Analyst3D.TinNodeFilter();
nodeFilter.FilterEnvelope = tinDataset.GetSuperNodeExtent();
nodeFilter.DataElementsOnly = false;
nodeFilter.SuperNode = true;
// search for hard edges
var edgeFilter = new ArcGIS.Core.Data.Analyst3D.TinEdgeFilter();
edgeFilter.FilterByEdgeType = true;
edgeFilter.EdgeType = ArcGIS.Core.Data.Analyst3D.TinEdgeType.HardEdge;

## Slide 27: Demo 1
3D Datasets

## Slide 28: 3D Analyst Layers
Uma Harano

## Slide 29: 3D Analyst Layers
3D Analyst datasets are visualized in a Map using their accompanying “Layer” object.
  Three types of 3D Layers are available.
    ArcGIS.Desktop.Mapping.SurfaceLayer base class
API support for 3D Layers include:
  Layer creation*
  Rendering*
  Analysis
  *Layer Creation and Rendering patterns are very similar for all 3D Layers.
  3D Layers are available in the ArcGIS.Desktop.Mapping namespace in ArcGIS.Desktop.Mapping assembly
Layer | Dataset
TinLayer | TinDataset
LasDatasetLayer | LasDataset
TerrainLayer | Terrain

## Slide 30: 3D Layer Creation
3D Layer creation follows the same pattern used for other ArcGIS Pro layers.
Use the CreateLayer method overloads in the LayerFactory class.
  CreateLayer overload that accepts the Uri for a datasource
  CreateLayer<T> (templated flavor) method that accepts a “LayerCreationParams” object.
public T CreateLayer<T>(LayerCreationParams layerParams, ILayerContainerEdit container) where T : Layer
public Layer CreateLayer(Uri dataUri, ILayerContainerEdit container, int index = 0, string layerName = "")

## Slide 31: 3D Layer creation
CreateLayer overload
1. CreateLayer overload that accepts the Uri for a layer datasource:
  Cast the result to a TinLayer, TerrainLayer or LasDatasetLayer.
  Layer is automatically added to the Map.
//Create TIN layer and add it to the map container
var tinUri = new Uri(@"d:\Data\Tin\TinDataset");
var tinLayer = LayerFactory.Instance.CreateLayer(tinUri, map) as TinLayer;
//Create LAS layer and add it to the map container
var lasUri = new Uri(@"d:\Data\Las\Netherlands.zlas");
var lasLayer = LayerFactory.Instance.CreateLayer(lasUri, map) as LasDatasetLayer;
//Create Terrain layer and add it to the map container
var terrainUri = new Uri(@"d:\Data\napa_county.gdb\napa\napa_Terrain");
var terrainLayer = LayerFactory.Instance.CreateLayer(terrainUri, map) as TerrainLayer;
TIN Layer
LASDatasetLayer
Terrain Layer

## Slide 32: 3D Layer creation
CreateLayer overload – Preconfigured 3D layer added to the map
CreateLayer<T> method that accepts a “LayerCreationParams” object:
  Use the TinLayer, TerrainLayer or LasDatasetLayer in the Layer Type template parameter.
  Options such as visibility, name, and renderers are pre-defined using the LayerCreationParams base class.
var tinParams = new TinLayerCreationParams(tinDataset) {
Name = "My TIN Layer", IsVisible = true, RendererDefinitions =...
};
var tinLayer = LayerFactory.Instance.CreateLayer<TinLayer>(tinParams, map);
var lasParams = new LasDatasetLayerCreationParams(lasUri){
Name = "My LAS Layer", IsVisible = true, RendererDefinitions =...
};
var lasLayer = LayerFactory.Instance.CreateLayer<LasDatasetLayer>(lasParams, map);
var terrainPrms = new TerrainLayerCreationParams(terrainUri){
Name = "My Terrain Layer", IsVisible = true, RendererDefinitions =...
};
var trnLyr = LayerFactory.Instance.CreateLayer<TerrainLayer>(terrainPrms, map);
TinLayer
LasDatasetLayer
TerrainLayer

## Slide 33: 3D Renderers
Renderers are objects that store symbolization for layers, to visualize the data in Pro.
Feature layers can only have one renderer.
  based on geometry type – points, lines and polygons.
3D Layers have multiple visualizations due to the nature of the data.
  – Ex. Tin layers have Nodes, edges, triangles
- Multiple Renderers can be assigned to each 3D Layer
  - Each renderer targeting each geometry.
Rendered with points
Rendered with lines
Rendered with polygons/Surface
Points, Lines and Polygons

## Slide 34: SurfaceRendererTarget enumeration
3D Layers can have multiple renderers assigned to the layer
  each renderer can target a different feature surface type.
The enumeration SurfaceRendererTarget reflects these different surface targets.
    SurfaceRendererTarget.Surface
SurfaceRendererTarget.Points
SurfaceRendererTarget.Edges
    SurfaceRendererTarget.Contours
Terrain layers: Can also be visualized by their “DirtyArea”
SurfaceRendererTarget.DirtyArea

## Slide 35: TinRendererDefinition class
Abstract base class definition for all 3D Layer Renderers.
  Available in the ArcGIS.Desktop.Mapping namespace
Use the various derived classes to create 3D Layer renderer definitions.
Derived classes expose properties to create renderers to draw faces, edges, nodes, breaklines, and contours.
  Symbols
  Name
  Description

## Slide 36: TIN layer renderers
https://github.com/Esri/arcgis-pro-sdk/wiki/ProConcepts-3D-Analyst-Layers
Maximum of 4 renderers per TIN layer
  Nodes
  Contours
  Edges
  Surfaces

## Slide 37: Terrain layer renderers
https://github.com/Esri/arcgis-pro-sdk/wiki/ProConcepts-3D-Analyst-Layers
Maximum of 5 renderers per Terrain layer
  Nodes
  Contours
  Edges
  Surfaces
  DirtyArea

## Slide 38: LAS Layer renderers
https://github.com/Esri/arcgis-pro-sdk/wiki/ProConcepts-3D-Analyst-Layers
Maximum of 4 renderers per LAS Dataset layer
  Nodes
  Contours
  Edges
  Surfaces

## Slide 39: Create 3D Renderer
Creating 3D renderers follows the same pattern used by other Pro layers.
Three steps to create renderers using the ArcGIS Pro API:
Create a “RendererDefinition” object to define the symbology to use.
  All derive from the base class TinRendererDefinition, many flavors available.
Use “CreateRenderer” method on the 3D layer to create a “CIMTinRenderer” object.
    CIMTinRenderer is a base class, many flavors available
    Pass in the TinRendererDefinition
Use the “SetRenderer” method on the 3D Layer to set the feature’s renderer.
  Pass in the CIMTinRenderer as first parameter
  Use the enumeration SurfaceRendererTarget to specify the surface type
    Contours, Edges, Points, Surface, DirtyArea

## Slide 40: Create 3D Renderer
//Step 1: Create renderer definition objects for the node, edge and surface renderers
var nodeRendererDef = new TinNodeRendererDefinition() { };
var edgeRendererDef = new TinEdgeRendererDefintion() { };
var surfaceRendererDef = new TinFaceRendererDefinition() { };
//Step 2: Create renderers
var nodeRenderer = tinLayer.CreateRenderer(nodeRendererDef);
var edgeRenderer = tinLayer.CreateRenderer(edgeRendererDef);
var surfaceRenderer = tinLayer.CreateRenderer(surfaceRendererDef);
//Step 3: Set the renderers on the TinLayer
tinLayer.SetRenderer(nodeRenderer, SurfaceRendererTarget.Points);
tinLayer.SetRenderer(edgeRenderer, SurfaceRendererTarget.Edges);
tinLayer.SetRenderer(surfaceRenderer, SurfaceRendererTarget.Surface);
//At this point the Tin layer has 3 renderers.

## Slide 41: Access Renderers from 3D Layer
Renderers in a 3D layer can be accessed in two ways.
Method 1: Obtain the renderers of the TinLayer using the GetRenderers() method.
  returns a readonly list of CIMTinRenderer.
Method 2: Use the GetRenderersAsDictionary() method to obtain the renderers in a dictionary structure according to SurfaceRendererTarget.
// get the renderers as a list
IReadOnlyList<CIMTinRenderer> tinRenderers = tinLayer.GetRenderers();
// get the renderers as a dictionary
Dictionary<SurfaceRendererTarget, CIMTinRenderer> rendererDict
= tinLayer.GetRenderersAsDictionary();
CIMTinRenderer edgeRenderer = rendererDict[SurfaceRendererTarget.Edges];

## Slide 42: Remove Renderers
You can also remove a specific renderer from the TinLayer by specifying the type using the SurfaceRendererTarget enumeration.
tinLayer.RemoveRenderer(SurfaceRendererTarget.Contours);

## Slide 43: 3D Layer Creation and Rendering demo
Uma Harano

## Slide 44: Line of Sight Analysis - TIN Layers
Uma Harano

## Slide 45: GetLineOfSight Method
Definition
Performs a line-of-sight analysis for an observer and target point on the TIN surface.
  Target’s visibility from observer
  Creates a “line of sight” that drapes over the TIN surface
    Visible line (possibly a multipart)
    Invisible line (possibly a multipart)
    Obstruction point, if any.

## Slide 46: GetLineOfSight Method
GetLineOfSight Method is available in the ArcGIS.Desktop.Mapping.TinLayer class.
Three steps to perform the line-of-sight analysis.
Step1: Instantiate the LineOfSightParams class.
  Input for the GetLineOfSight method.
      TargetPoint
      ObserverPoint
      OutputSpatialReference
      Note: Also, advanced options:
        TargetHeightOffset, ObserverHeightOffset, ApplyCurvature, ApplyRefraction, etc….
//Step 1: Set the input values for the Line-of-Sight analysis
LineOfSightParams lineOfSightParams = new LineOfSightParams();
lineOfSightParams.TargetPoint = targetPt;
lineOfSightParams.ObserverPoint = observerPoint;
lineOfSightParams.OutputSpatialReference = mapView.Map.SpatialReference;

## Slide 47: GetLineOfSight Method
Step 2: Use CanGetLineOfSight() method.
  Determines whether a Line-of-Sight analysis can be calculated for the given set of parameters in the LineOfSightParams class.
    Return true if the parameters are valid, false if the parameters are not valid.
    Do your points lie on the TIN surface?
    Note: if you are using advanced options, your TIN Surface:
      Must use a projected coordinate system
      Have Z Coordinate units defined
LineOfSightParams lineOfSightParams = new LineOfSightParams();
…
//Step 2: Determines if the Line-of-sight analysis can be calculated
if (tinLayer.CanGetLineOfSight(lineOfSightParams)) {
…

## Slide 48: GetLineOfSight Method
Step 3: Execute GetLineOfSight method on the TIN layer.
  Returns a LineOfSightResult class that contains the results of the analysis.
  Key properties of the LineOfSightResult class:
    IsTargetVisibleFromObserverPoint
    VisibleLine, InvisibleLine
    ObstructionPoint
LineOfSightParams lineOfSightParams = new LineOfSightParams();…
if (tinLayer.CanGetLineOfSight(lineOfSightParams)) {
//Step 3: Run the analysis
LineOfSightResult loSResult = tinLayer.GetLineOfSight(lineOfSightParams);

## Slide 49: GetLineOfSight Method
LineOfSightParams
//Step 1: Set the input values for the Line-of-Sight analysis
LineOfSightParams lineOfSightParams = new LineOfSightParams();
lineOfSightParams.TargetPoint = targetPt;
lineOfSightParams.ObserverPoint = observerPoint;
…
//Step 2: Determines if the Line-of-sight analysis can be calculated
if (tinLayer.CanGetLineOfSight(lineOfSightParams)) {
//Step 3: Run the analysis
LineOfSightResult loSResult = tinLayer.GetLineOfSight(lineOfSightParams);
Polyline visibleLine = loSResult.VisibleLine;
Polyline invisibleLine = loSResult.InvisibleLine;
MapPoint onstructionPoint = loSResult.ObstructionPoint;
bool isTargetVisibleFromObserverPoint = loSResult.IsTargetVisibleFromObserverPoint;
}

## Slide 50: GetLineOfSight Demo
Uma Harano

## Slide 51: LAS Points
LasPoint
  Stores x, y, z values
    Coordinate2D, Coordinate3D, ToMapPoint
  PointID (base index is 1. Not 0)
  FileIndex (base index is 0)
  ClassCode
  ReturnNumber
  NumberOfReturns
  Flags
    IsKeyPoint, IsOverlapPoint, IsSyntheticPoint, IsWithheld

## Slide 52: Accessing LAS Points
Using Point ID
  GetPointByID
LAS dataset can reference multiple LAS files, so more than one point with the same pointID can be found.
  Specify an extent
  Specify the file index
// get points by ID
// could be more than 1 point if multiple LAS files are referenced
var points = lasDataset.GetPointByID(123456);
// use an envelope.
// there could still be more than 1 point if multiple LAS files are referenced
var points = lasDataset.GetPointByID(123456, envelope);
// use a file index to be specific
var point = lasDataset.GetPointByID(2, 123456);

## Slide 53: Accessing LAS Points
Search with a filter
  SearchPoints
  Similar pattern to searching a feature class for features
    Parameter is a filter object – LasPointFilter
    Pass null to find all points
    Returns a cursor – LasPointCursor
// search all points
using (LasPointCursor ptCursor = lasDataset.SearchPoints(null))
{
while (ptCursor.MoveNext())
{
using (ArcGIS.Core.Data.Analyst3D.LasPoint point = ptCursor.Current)
{
}
}
}

## Slide 54: LAS Filter
FilterGeometry
  Specify an extent to search. Default is null meaning the entire extent is used.
ClassCodes
  Specify a set of classification codes. Default is null.
Returns
  Specify a set of return values. Default is null.
Flags
  KeyPoints, OverlapPoints, SyntheticPoints. Default is true.
  WithheldPoints. Default is false.

## Slide 55: Accessing LAS Points
// search within an extent
var pointFilter = new LasPointFilter();
pointFilter.FilterGeometry = envelope;
using (LasPointCursor ptCursor = lasDataset.SearchPoints(pointFilter))
{
...
}
// search within an extent and limited to specific classification codes
var pointFilter = new LasPointFilter();
pointFilter.FilterGeometry = envelope;
pointFilter.ClassCodes = new List<int>() {4, 5 };
using (LasPointCursor ptCursor = lasDataset.SearchPoints(pointFilter))
{
...
}

## Slide 56: LAS Display Filter
Manipulate which points and surface constraints are drawn to improve analysis and visualization.
Use the LasPointDisplayFilter class
Set according to
  FilterType – coarse grained – All Points, Ground Points, Non GroundPoints, First Return points
  Set of classification codes
  Set of return values
  Custom filter
    Combination of classification codes, return values and point flags.

## Slide 57: LAS Display Filter
// display only ground points
lasLayer.SetDisplayFilter(LassPointDisplayFilterType.Ground);
// display a set of classification codes
List<ing> classifications = new List<int>() {4, 5, 7, 10);
lasLayer.SetDisplayFilter(classifications);
// display a set of returns
List<LasReturnType> returns = new List<LasReturnType()
{LasReturnType.ReturnFirstOfMany};
lasLayer.SetDisplayFilter(returns);
// set a custom display filter
var newDisplayFilter = new LasPointDisplayFilter();
newDisplayFilter.Returns = new List<LasReturnType>() {LasReturnType.ReturnLasyOfMany};
newDisplayFilter.ClassCodes = new List<int>() {2, 4};
newDisplayFilter.KeyPoints = true;
newDisplayFilter.SyntheticPoints = false;
lasLayer.SetDisplayFilter(newDisplayFilter);

## Slide 58: LAS Surface Constraints
Active surface constraints can be incorporated into the display filter or they can be turned on or off individually.
Use LasDatasetLayer.SetActiveSurfaceConstraints
// get the constraints from the dataset
IReadOnlyList<SurfaceConstraint> constraints = lasDataset.GetSurfaceConstraints();
// get the set of active surface constraints on the layer
var activeSurfaceConstraints = lasDatasetlayer.GetActiveSurfaceConstraints();
// clear all surface constraints (i.e. none are active)
lasDatasetlayer.SetActiveSurfaceConstraints(null);
// set the first surface constraint active
List<string> newActive = new List<string>();
newActive.Add(constraints[0].DataSourceName);
lasDatasetLayer.SetActiveSurfaceConstraints(newActive);

## Slide 59: LAS – Searching the layer
Use the SearchPoints method on the layer with a LasPointFilter
Display filter is respected if it has been set
// search within an extent;
// only points that match the display filter (if set) and the search filter are returned
var pointFilter = new LasPointFilter();
pointFilter.FilterGeometry = envelope;
using (LasPointCursor ptCursor = lasDatasetLayer.SearchPoints(pointFilter)) {
while (ptCursor.MoveNext() {
using (LasPoint point = ptCursor.Current) {
}
} }

## Slide 60: Demo 4
LAS Analysis

## Slide 61: Summary
Datasets
  TinDataset, Terrain, LasDataset
Layers + creation
  TinLayer, TerrainLayer, LasDatasetLayer
  TinLayerCreationParams, TerrainLayerCreationParams, LasDatasetLayerCreationParams
Renderers
  TinRendererDefinition
Analysis
  Searching (TIN and LAS)
  Line of Sight (TIN)

## Slide 62: ArcGIS Pro SDK for .NET – Technical Sessions
Detailed Agenda: https://www.esri.com/en-us/about/events/devsummit/agenda/detailed
NOTE: Session titles are led by “ArcGIS Pro SDK for .NET” in online agenda
Date | Time | Session
Tue, Mar 12 | 1:00 PM - 2:00 PM | ArcGIS Pro SDK for .NET: Introduction to the Pro SDK (Mesquite B)
 | 2:30 PM - 3:30 PM | ArcGIS Pro: The Road Ahead (Smoketree A-E)
 | 4:00 PM - 5:00 PM | ArcGIS Pro SDK for .NET: Introduction to Map and Geodatabase Topology (Mesquite C)
 | 5:30 PM - 6:30 PM | ArcGIS Pro SDK for .NET: Approaches for Pro Extensibility (Mesquite C)
Wed, Mar 13 | 10:30 AM - 11:30 AM | ArcGIS Pro SDK for .NET: Introduction to the Editing API (San Jacinto, Renaissance)
 | 1:00 PM - 2:00 PM | ArcGIS Pro SDK for .NET: Asynchronous Programming for Addins 1 (Mesquite GH)
 | 2:30 PM - 3:30 PM | ArcGIS Pro SDK for .NET: Asynchronous Programming for Addins 2 (Mesquite GH)
Thu, Mar 14 | 4:00 PM - 5:00 PM | ArcGIS Pro SDK for .NET: What's New in the Geodatabase and Utility Network APIs
 | 4:00 PM - 5.00 PM | ArcGIS Pro SDK for .NET: Introduction to the 3D Analyst API (Mesquite GH)
 | 5:30 PM - 6:30 PM | ArcGIS Pro SDK for .NET: Introduction to the Knowledge Graph API (Mesquite C)

## Slide 63
ArcGIS Pro SDK for .NET – Demo theaters
NOTE: Session titles are led by “ArcGIS Pro SDK for .NET” in online agenda
Detailed Agenda: https://www.esri.com/en-us/about/events/devsummit/agenda/detailed
Date | Time | Session
Thu, Mar 14 | 11:15 AM - 11:45 AM | ArcGIS Pro SDK for .NET: Data Definition Language (DDL) in the ArcGIS Pro SDK
 | 1:00 PM - 1:30 PM | ArcGIS Pro SDK for .NET: 3D Analyst and TIN Layer Line of Sight
 | 1:45 PM - 2:15 PM | ArcGIS Pro SDK for .NET: An Overview of Catalog Layers in Pro
 | 2:30 PM - 3:00 PM | ArcGIS Pro SDK for .NET: Extending Editor Inspector UI with Embeddable Controls
 | 3:15 PM - 3:45 PM | ArcGIS Pro SDK for .NET: What's New for the Parcel Editing API

## Slide 64: Introduction to the 3D Analyst API
Questions?
    https://github.com/Esri/arcgis-pro-sdk/wiki/Tech-Sessions#2024-palm-springs

## Slide 65: Please Share Your Feedback in the App
Download the Esri Events app and find your event
Select the session you attended
Scroll down to “Survey”
Log in to access the survey

## Slide 66: Copyright © 2024 Esri. All rights reserved.